Tom Kunze, project manager MINI Cabrio.

Definitely in the exterior a highlight is the new colour and trim options we offer. An example here is the communication model, which is shown a MINI Cooper S in Interchange Yellow with 17 inch dark aluminum wheels, which stands out from the crowd. And most importantly for the Convertible of course is the soft top technology, which is by standard fully automatic and works up to 30 km/h, so you can open and close the soft top while driving slowly, very important feature for example when you caught by rain. And for our design orientated customers the colour and trim of the soft top. The base of course is classic black, but we do offer two new colours, one is Hot Chocolate, very nice dark brown tone and a new Denim Blue soft top, which has a silver effect, which is a metallic thread woven into the soft top, which gives it a very interesting appearance under sunlight. And of course, the soft-top functionality including the sunroof, which can be open up to 40 cm until 120 km/h delivering fresh air as you like.